## Slide 1: Circuit Characterization Interconnects and Inverters
Class 4
ECE 4140/6240
M.E. Zaghloul
Fall 22

## Slide 2: Introduction
VLSI Design Parameters
- Speed
- Power
- Area
- Reliability
In this class we will learn how
- Estimate the Delay
- Estimate the Power
As the device size scales into the deep submicron, inter-chip wires will be very important parameters in the design

## Slide 3: nMOS I-V Summary
Shockley 1st order transistor models

## Slide 4: Non-Ideal Transistor Behavior
We Learned from last class that Non-ideal Transistor Behavior due to submicron size cause the following;
  High Field Effects lateral field between source and drain will cause
    Mobility Degradation
    Velocity Saturation
  Threshold Voltage Effects Vt is not constant
    Body Effect ϒ
    Drain voltage creates electric field that affects the threshold voltage
    For Short Channel the threshold voltage increases with channel length
  Leakage small amount of current when transistor Id OFF
    Subthreshold Leakage
    Gate Leakage
    Junction Leakage
    In Addition to Environment Variations
Environmental Variations Temperature Dependence and Power supply variations , and Geometry dependence.

## Slide 5: The wire- Interconnects Chapter (4 in text)
It is important for the designer to have clear insight into the parasitic wiring effect
Each wire in the circuit is considered as conductor with parasitic capacitance, parasitic resistance, and parasitic inductor.

## Slide 6: Interconnect Impact on Chip

## Slide 7: Wire Models
All-inclusive model
Resistor, Inductor, and
Capacitor
Capacitance-only

## Slide 8: Impact of Interconnect Parasitic
Interconnect parasitic
  reduce reliability
  affect the performance that is speed and the power consumption
Classes of parasitic
  Capacitive
  Resistive
  Inductive

## Slide 9: RC Delay of the Interconnect and Inverter
We would like to calculate the parasitic R and C of the wire to estimate how much delay is in the wire. Delay is RC = Time
In addition we would like to estimate how much delay in the device (the transistor). This mean we have to estimate the effective resistance of the transistor and the parasitic capacitance

## Slide 10: Simplification for the wire
Inductive effect can be ignored if the resistance of the wire is high, long wire with small cross section
For short wire with large cross section capacitance are important
Interwire capacitance are important when wires run in parallel for long distance

## Slide 11: Capacitance of Wire Interconnect

## Slide 12: Capacitance: The Parallel Plate Model
Rectangular wire placed above semiconductor substrate
R = ρL = ρ L
A
W H

## Slide 13: Permittivity Different Materials

## Slide 14: The Parallel Plate Model Capacitances
Too simple for small ratio of W/H, the Parallel plate model is not accurate (As the dimensions are in Deep submicrons)
The Capacitance between the side wall can no longer be ignored “Fringe Capacitance” specifically at high frequency
The total capacitance is the sum of Parallel plate and Fringe

## Slide 15: Fringing Capacitance
The model numerical (Approx.) decompose the capacitance into two components
PP
Fringe
Cylinder Model

## Slide 16: Fringing versus Parallel Plate
For W/H large PP dominate, while for W/H small Fringe dominate
CFringe
To Illustrate The Importance of fringe as W/H decrease

## Slide 17: Capacitive Coupling
Each wire is not only coupled to the ground, but also to the neighboring wires on the same layer and on adjacent layers
This will affect the noise in the circuit and the performance of the chip

## Slide 18: Interwire Capacitance

## Slide 19: Impact of Interwire Capacitance
Interwire capacitance become a dominant factor in multilayers interconnect structures
As the technology scales

## Slide 20: Wire Area and Fringe Capacitance Values
The following table shows 0.25 um CMOS process
The table rows represent the top plate of the capacitor
The columns represent the bottom plate
The areas are expresses in aF|um

## Slide 21: Wiring Capacitances (0.25 mm CMOS) in aF/um-page 143
Twice as thick as other metals
Bottom Thick Field Oxide
Shaded area are Fringe

## Slide 22: Page 144 Rabaey example 4.1

## Slide 23: Consider each element
The properties of Resistances
How to calculate the parameters of the Resistances

## Slide 24: Wire Resistance
Sheet resistance have units Ω/square
R = Sheet resistance * L/W = Rs L/W
H is constant for a technology

## Slide 25: Resistive Model of the wire
The model is too simplistic
To have the above model it is desirable to keep the cross section of the wire as large as possible to minimize the resistance( WxH)
To have denser wiring it is desirable to have smaller W
As result we have seen steady reduction of the ratio W/H

## Slide 26: Interconnect Resistance

## Slide 27: Dealing with Resistance
Selective Technology Scaling
Use Better Interconnect Materials
  reduce average wire-length
  e.g. copper, silicides
  Do-not Use Polysilicon for routing
More Interconnect Layers
  reduce average wire-length

## Slide 28: Dealing with Resistance
Use of Diffusion wires should be avoided due to the large capacitances
Transitions between routing layers add extra resistance to a wire called contact resistance
Keep signal wires on a single layer whenever possible

## Slide 29: Advanced Process 0.18, 0.13µ
Advanced Processes offer different material such silicide, high conductive material (Mixture of silicon and metal)
Gates of MOS are fabricated with top layer of Silicide to reduce the gate resistance
Recently Metal gate transistor

## Slide 30: Polycide Gate MOSFET
n
+
n
+
SiO
2
PolySilicon
Silicide
p
Silicides: WSi
2,
TiSi
2
, PtSi
2
and TaSi
Conductivity: 8-10 times better than Poly

## Slide 31: Sheet Resistance for Different layers

## Slide 32: Example: Intel 0.25 micron Process
5 metal layers
Ti/Al - Cu/Ti/TiN
Polysilicon dielectric

## Slide 33: Skin Effect
We have considered the resistance to be linear and constant
At high frequency the resistance becomes function of the frequency (skin effect)
High frequency current tends to flow primary on the surface of the conductor with skin depth δ.
Increase resistance
δ

## Slide 34: Skin Effect
The skin depth is defined as the depth at which the current falls off to the value of e-1
For aluminum at 1 GHz, the skin depth equals 2.6 μm
There is a critical frequency fs below which the whole wire is conducting current.
Clock wires tend to carry the highest frequency, and are always wide to reduce resistance. Skin effect is likely

## Slide 35: Inductance
The inductance is related to the voltage and the current by
A simpler approach is to relate cl = ε μ , where c is the capacitance per unit length and l is inductance per unit length ( this is derived from Maxwell), € is permittivity andµ is permeability

## Slide 36: Inductance
The speed of propagation depends on the inductance and the capacitance and thus depends on the permeability and permittivity of the surrounding dielectric
Inductance is only an issue in integrated circuits at the high end of the performance curve

## Slide 37: Electric Wire Modeling
In this section we will look at the equations of the wire and include parasitic
These parasitic elements have an impact on the electrical behavior of the circuit
The simple model of voltage change at one end will simply propagate to the other end is not applicable for small dimensions
Notice that we are trying to see the effect on the Speed

## Slide 38: How To Model the Wire
Consider Distributed capacitance as shown in the figure
It can be Lumped as shown in the following example

## Slide 39: The Lumped Model
Clumped =Cwirex L
Ideal model assuming the same voltage at every segment
Cwire is
the capacitance
per unit length

## Slide 40: Calculating the Delay
Metal wires more than few millimeters have significant resistance
The lumped capacitor model is no longer adequate
Resistive capacitor model have to be adopted

## Slide 41: Lumped R-C model
The capacitive lumped model is simple and most popular
On chip the wires are few millimeters in length and have significant resistance
We first look at the lumped RC model

## Slide 42: Lumped RC model
The first Approach is lump the total wire resistance of each wire into single resistance
Similarly combines the global capacitances into single capacitance

## Slide 43: Elmore Delay Lumped Model Non - Branched RC
ΤDi = C1R1+ C2( R1+ R2) + … + Ci( R1+ R2+…Ri)

## Slide 44: Time Constant RC Wire model Distributed RC
The model can be used to approximate the RC delay in long wire
Assume wire with total length L partitioned into equal segments N, segment length L/N
The resistance will be rL/N, capacitance will be cL/N, where r and c are per unit length
Using Elmore model page 155( in Rabaey) to get the total delay

## Slide 45: Time Constant RC Wire model Distributed RC

## Slide 46: The Model Presented on Page 43
can be used to approximate the resistance capacitive wire
The wire with total length of L is partitioned into N identical segmentseach with L/N length

## Slide 47: Distributed Wire Model
Assume: Wire modeled by N equal-length segments
For large values of N:
R= rL
C = cL

## Slide 48: Time Constant RC Wire model
From the above Formula we see that the delay is quadratic function of the length L
The delay of the distributed rc line is one half the lumped model
Lumped RC model is pessimistic model for RC wire as compared to distributed model
The distributed model is more appropriate

## Slide 49: Distributed rc line
In the previous discussion we showed that the RC model is a pessimistic model for the resistive –capacitive wire, and distributed rc model is more appropriate

## Slide 50: Distributed rc Line
r is resistance per unit length, c is capacitance per unit length
The schematic representation is as shown
The correct behavior is obtained by the diffusion equation

## Slide 51: The Distributed RC-line
The diffusion equation
It can be represented by diffusion equation

## Slide 52: Simulation of Step-response of RC wire as a function of time
Solution of the Differential Equation as function of time and place
The waveform rapidly degrades for long wires

## Slide 53: The Previous Figure
Shows the response of a wire to step input
Plotting the wave forms at different points in the wire as a function of time
Observe the step waveform diffuse from the start to the end of the wire, and the waveform rapidly rapidly degrades

## Slide 54: Design Rules of Thumb
Table 4-7 ( page 158-Rabaey) shows the delay of Lumped and distributed RC networks
rc delays should only be considered when tpRC >> tpgate of the driving gate
Time delay 0.69% lumped and 0.38RC distributed Voltage 0-50% voltage range drop
This will define critical length of the wire
0.38RC >> tpgate
Lcrit >>
R = rL, and C = c L
rc delays should only be considered when the rise (fall) time at the gate input is smaller than RC, the rise (fall) time of the line
  trise < RC

## Slide 55: Design Rule
When the designer analyze the interconnect network –to consider the effect of the RC delay and if it will be considered or can get away with a simple lumped capacitive model
Simple rule
rc delays should be considered only when tpRC
is comparable or larger than tpgate of the driving gate

## Slide 56: Transmission line
When the switching speeds become sufficiently fast the inductance of the wire starts to dominate the delay behavior and transmission line effect must be considered
TR line effect must be already considered for deep submicron ( Technology Now ) designs
Transmission line effect should be considered when the rise and the fall time of the input signal is smaller than the time of flight of the transmission line

## Slide 57: Summary
We will not discuss section 4.4.5 Transmission line in Rabaey book
The simulation tools should calculate the wire parasitic
This chapter presented in depth analysis of the behavior of the interconnect wire
One should always differentiate between global interconnection and local( what is local and Global interconnect)
Constant delay is predicted for local wire, while for global wire it increases 50% per year
Wire delay is starting to play a predominant role in today digital design

## Slide 58: CMOS Inverter Chapter 5
ECE6140/6240
Fall 2022

## Slide 59: The CMOS Inverter: A First Glance
V
in
V
out
C
L
V
DD

## Slide 60: CMOS Inverter
Polysilicon
In
Out
V
DD
GND
PMOS
2l
Metal 1
NMOS
Contacts
N Well

## Slide 61: Two Inverters
Connect in Metal
Share power and ground
Abut cells

## Slide 62: CMOS Inverter First-Order DC Analysis
VOL = 0
VOH = VDD
VM = f(Rn, Rp)
V
DD
V
DD
V
in
=
V
DD
V
in
=
0
V
out
V
out
R
n
R
p
Switch model of
CMOS inverter

## Slide 63: Delay Definitions

## Slide 64: Important Reference Points
Propagation delay Τp defined as 50% of final voltage value
Tp is calculated as .38RC ( distributed) and .69RC ( Lumped)
Rise time Tr is the time to reach 90% of the final voltage
Fall time Tf is the time to reach 10% of the final voltage
( these results are from applying step response to lumped and distributed RC circuit)

## Slide 65: Delay Estimation
We would like to be able to easily estimate delay
  Not as accurate as simulation
  But easier to ask “What if?”
The step response usually looks like a 1st order RC response with a decaying exponential.
Use RC delay models to estimate delay
  C = total capacitance on output node
  Use effective resistance R
  So that tpd = RC
Characterize transistors by finding their effective R
  Depends on average current as gate switches

## Slide 66: Properties
The logic levels at the output are not dependent on the relative sizes of the transistors, transistors can be minimum size
There is always a path from power supply or Ground to output. Well designed inverter have low output impedance less noise
The input resistance of the CMOS inverter is extremely high

## Slide 67: DC Operation: Voltage Transfer Characteristic

## Slide 68: CMOS Inverter VTC

## Slide 69: CMOS Inverter Region of Operation
0< Vin< VTh , p-Linear, n-Off
VTH < Vin < VDD/2, p-linear,n-Sat
Vin = VDD/2 , P-Sat, n- Sat
VDD/2 < Vin< VDD- VTH, P-Sat, n-Linear
Vin> VDD – VTH , P-Off, n-Linear

## Slide 72: CMOS Inverter Load Characteristics

## Slide 73: CMOS Inverter: Transient Response
t
pHL
= f(R
on
.C
L
)
= 0.69 R
on
C
L
V
out
V
out
R
n
R
p
V
DD
V
DD
V
in
5
V
DD
V
in
5
0
(a) Low-to-high
(b) High-to-low
C
L
C
L
Switch model of
Dynamic Behavior
of CMOS inverter

## Slide 74: Gate Response
The fast gate is built either by keeping the output capacitance small or by decreasing the on-resistance of the transistor
The resistance is inversely proportion to W/L ratio, to decrease resistance increase W/L

## Slide 75: RC Delay Model
Use equivalent circuits for MOS transistors
  Ideal switch + capacitance and ON resistance
  Unit nMOS has resistance R, capacitance C
  Unit pMOS has resistance 2R, capacitance C
Capacitance proportional to width
Resistance inversely proportional to width

## Slide 76: Simulated VTC ( voltage Transfer characteristics )
V m is the Switching Threshold

## Slide 77: Switching Threshold
VM is the switching threshold the point at which Vin = Vout
At this region both PMOS and NMOS are in saturation
Analytical expression is obtained by equating the current through the two devices

## Slide 78: Switching Threshold as a function of Transistor Ratio
10
0
10
1
0.8
0.9
1
1.1
1.2
1.3
1.4
1.5
1.6
1.7
1.8
M
V
(V)
W
p
/W
n

## Slide 79: Switching Threshold
VM is relatively insensitive to variations of device ratio W/L
The effect of changing Wp to Wn is to shift the VTC, increasing the width of PMOS or the NMOS moves VM toward VDD or toward ground, this is sometime is useful

## Slide 80: Mapping between analog and digital signals
Simple approach to
Approximate VTC

## Slide 81: Piecewise Linear Approximation of VTC
VOUT
VIN
VOH
VOL
VIL
VIH
VM
Slope is g
Inverter is amplifier
With gain -g

## Slide 82: Noise Margin Determining VIH and VIL Simple PWL Model
A simplified approach to VTC slope of the line is -g
g is the gain
g = -dVout/dVin

## Slide 83: Mapping between analog and digital signals
Simple approach to
Approximate VTC

## Slide 84: Noise Margins Determining VIH and VIL
Vin
Vout
VOH = VDD
VM
By definition, VIH and VIL are where dVout/dVin = -1 (= gain)
VOL = GND
A piece-wise linear approximation of VTC
NMH = VDD - VIH
NML = VIL - GND
Approximating:
VIH = VM - VM /g
VIL = VM + (VDD - VM )/g
So high gain in the transition region is very desirable
Notes: A high gain in the transition region is VERY desirable. In the extreme case of an infinite gain, the noise margins simplify to VOH – VM and VM – VOL for NMH (ideally, VDD – VM) and NML (ideally, VM – GND), respectively, and span the complete voltage swing.

## Slide 85: Definition of Noise Margins

## Slide 86: The gain of the Inverter
The midpoint gain at which the PMOS and NMOS are in saturation
The gain is dVout / dVin
Obtain the equation for Vout as function of Vin by equating the current at the switching voltage and considering the channel modulation

## Slide 87: Gain Determinates
Vin
gain
Gain is a strong function of the slopes of the currents in the saturation region, for Vin = VM
Determined by technology parameters, especially channel length modulation (λ).
Gain g =
Obtain the current equation for PMOS and NMOS, assuming devices in velocity saturation, and considering channel modulation

## Slide 88: Inverter Gain

## Slide 89: Gain as a function of VDD
Gain=-1
Reducing voltage VDD improves gain
It is worse for very low power supply

## Slide 90: Scaling Power Supply
Reducing power supply reduce power (good) how about the delay?
The DC characteristics become sensitive to variations in the device parameters such as threshold voltage
Reducing supply voltage means reducing noise (internal noise) , circuit is more sensitive to external noise

## Slide 91: Impact of Process Variations
0
0.5
1
1.5
2
2.5
0
0.5
1
1.5
2
2.5
V
in
(V)
V
out
(V)
Good PMOS
Bad NMOS
Good NMOS
Bad PMOS
Nominal

## Slide 92: Impact of Process Variation on VTC Curve
Vin (V)
Vout (V)
Nominal
Good PMOS
Bad NMOS
Bad PMOS
Good NMOS
Process variations (mostly) cause a shift in the switching threshold
Smaller oxide
Thickness, Smaller
Length, Width
Notes: A good device has a small oxide thickness (-3nm), a small length (-25nm), a higher width (+30nm) and a smaller threshold (-60mV). The opposite is true for a bad device.

## Slide 94: Dynamic Behavior of Inverter
Time Delay and Power
Next Class